# pyg2p 2.1

Version	2.1
Author	Domenico Nappo (domenico.nappo(at)gmail.com)
Release Date	2016-09

## Introduction
pyg2p is a tool to convert GRIB files into PCRASTER maps.
It reads georeferenced variables from GRIB version 1 and 2 files and it produces PCRaster maps, after some manipulation steps (conversion, aggregation). Execution parameters are passed via command line arguments and/or JSON template files.
Manipulations are completely configurable in execution JSON files and are of three types:

- conversion (formulas are to configure in parameters.json)
- correction (correction formulas are based on DEM maps and geopotential message and are to be configured in templates)
- aggregation (accumulation or average).

The interpolation mode is also configurable and it's needed to resample the input GRIB grid to the PCRaster target grid (which is determined by latitude and longitudes maps).
What you need to execute conversion with pyg2p version 2.0 is enlisted below:
1. The input grib file that contains the variable you want to convert, identified by its shortName
2. The geopotential message in a separate grib file (if not included with input grib file), for temperature altitude correction.
3. PCRaster coordinate maps (latitudes and longitudes) of target GRID for interpolation. DEM of target GRID for correction.

## Installation
To install package, you can use a python virtual environment or directly install dependencies and package at system level (executable script will be saved into /usr/local/bin in this case).
IMPORTANT: Before to launch setup, you need to configure geopotentials and intertables paths in configuration/global/global_conf.json. These paths are used by pyg2p to read geopotentials and intertables already configured. You may need to download files from FTP (use -W option for this). Users running pyg2p installed by a different user (ie. root) will configure similar paths for their own intertables and geopotentials under his home folder. These paths will need write permissions.
Grab last archive and follow these steps:
$ tar xzvf pyg2p.tar.gz
$ cd pyg2p
$ vim configuration/global/global_conf.json # to edit shared paths !!!
$ python setup.py install

After installation, you will have all dependencies installed and an executable script 'pyg2p' (in a virtual environment, script is located under <VIRTUALENV_PATH>/bin folder otherwise under /usr/local/bin). Some python packages can be problematic to install at first shot. Read following paragraph for details.

### Manual installation of dependencies

Default setup.py may have troubles in installing dependencies or you may prefer to install them manually.
Check this table to install dependencies manually (follow the order) and try to install again.

Python packages
NumPy>=1.10.1	Scientific packages for array operations and reading/writing encoded files. They depends on several C libraries that must exist on your system before to proceed. / $pip install numpy>=1.10.1 / $pip install numexpr / $pip install scipy>=0.16.0 / $pip install GDAL / * If you have GDAL C/C++ libraries already installed on your system, you might need to install the exact GDAL python matching the C GDAL version. / ** For gribapi python package, please refer to GRIB API documentation.
Numexpr>=2.4.6
SciPy>=0.16
gribapi*
GDAL python**
netcdf4-python	Please, refer to http://unidata.github.io/netcdf4-python/ for details
dask[array] dask[bag] / toolz	Light packages for parallelization (used in GRIB API interpolation methods): / $pip install toolz / $pip install dask[bag] / $pip install dask[array]
xmljson	Used only to convert old XML pyg2p v1 to v2 JSON format (-C command line argument): / $pip install xmljson
memory_profiler (optional)	Memory usage information for test suite (for development). / $pip install memory_profiler $pip install psutil

### Migrating from v 1.x
If you migrate from a pyg2p version 1.x, you can convert existing XML configuration files to json (execution command files, parameters.xml and geopotentials.xml) and also convert old intertables (only grib api methods intertables).
1. Copy all your old XML configuration into a folder ./xml_backup. You can create different subfolders for convenience because conversion will be recursive.
2. Convert files (recursively) from XML to JSON with command:
   $pyg2p.py -C ./xml_backup
3. Copy parameters.json and geopotentials.json from ./xml_backup into user folder ~/.pyg2p/
4. Copy your geopotential files to folder defined in your .conf file in GEOPOTENTIALS variable.

You can also convert your existing interpolation tables made with pyg2p version 1.x GRIB_API methods to be compliant with new format. New files will be copied under folder defined in INTERTABLES variable and intertables.json configuration will be updated during conversion.

$pyg2p.py -z <path_to_convert>
Note: Intertables for rotated grids are not valid (GRIB_API 1.14.4) so they won't be converted. You need to configure scipy interpolation methods for this kind of grid for the time being.

Intertables created with scipy methods cannot be converted but they are generally quite fast to create (seconds or minutes).
## Configuration

One of the things to configure for any user running pyg2p, is GEOPOTENTIALS and INTERTABLES variables with paths to folders with write permissions.
NOTE: From version 2.1, the user needs to setup these variables only if he/she needs to write new interpolation tables (option -B [-X]) or to add new geopotentials from grib files (option -g).
These variables contains user paths and must be configured in a .conf file (e.g. paths.conf) under ~/.pyg2p/ directory. This can look like:
GEOPOTENTIALS=/dataset/pyg2p_data_user/geopotentials
INTERTABLES=/dataset/pyg2p_data_user/intertables

User intertables (for interpolation) are read/write from INTERTABLES and geopotentials (for correction) are read from GEOPOTENTIALS.
Pyg2p will use its default configuration for available intertables and geopotentials. These are read from paths configured during installation in global_conf.json.
If you need to download default files from ECMWF FTP, just launch pyg2p with -W option and the dataset argument (argument can be geopotentials or intertables) and files are saved in user paths configured above:

$pyg2p -W intertables

You can edit FTP authentication parameters in ~/.pyg2p/ftp.json

### Advanced configuration
User json configuration files are empty. If you need a new parameter or geopotential that is not configured internally in pyg2p, you can setup new items (or overwrite internal configuration).
#### Adding a parameter to ~/.pyg2p/parameters.json
If you are extracting a parameter with shortName xy from a grib file that is not already globally configured, add an element as shown below (only part in bold has been added):

{
"xy": { "@description": "Variable description",
   "@shortName": "xy",
   "@unit": "unitstring"
},
}

You can configure (more than) a conversion element with different ids and functions. You will use shortName and conversionId in the execution JSON templates.

{
"xy": { "@description": "Variable description",
   "@shortName": "xy",
   "@unit": "unitstring"
},
"xyz": {
    "@description": "Variable description",
    "@shortName": "xyz",
    "@unit": "unitstring/unistring2",
    "Conversion": [
        {
        "@cutOffNegative": true,
        "@function": "x=x*(-0.13)**2",
        "@id": "conv_xyz1",
        "@unit": ”g/d"
        },
        {
        "@cutOffNegative": true,
        "@function": "x=x/5466 - (x**2)",
        "@id": "conv_xyz2",
        "@unit": "g/h"
        }
       ]
        },

}
Note: Aware the syntax of conversion functions. They must start with x= followed by the actual conversion formula where x is the value to convert. Units are only used for logging.

#### Adding a geopotential for correction
If the input grib file has a geopotential message, pyg2p will use it for correction. Otherwise, it will read the file from user data paths or global data paths.
To add a geopotential GRIB file to pyg2p configuration, use this command:
$pyg2p -g path_to_geopotential_grib
This will copy the file to folder defined in GEOPOTENTIALS variable and will update geopotentials.json with the new item.
#### Interpolation tables
Interpolation tables are read from user or global data folders.
If the table is missing, it will create it into user data folder for future interpolations (you must pass -B option to pyg2p).
Depending on source and target grids size, and on interpolation method, table creation can take from minutes to days. To speed up interpolation table creation, use parallel option -X to have up to x6 speed gain.
### Execution templates
Execution templates are JSON files that you will use to configure a conversion. You will pass path to the file to pyg2p with command line option'-c'.
Most of options can be both defined in this JSON file and from command line. Note that command line options overwrite JSON template.
If you have a large set of conversions for same parameters, it's more convenient to define a single template where you define parameter, interpolation and aggregation and pass the rest of parameters from command line.
Here some examples of JSON commands files:

    {
        "Execution": {
        "@name": "Octahedral test 1",
        "Aggregation": {
        "@step": 24,
        "@type": "average"
        },
        "OutMaps": {
        "@cloneMap": "/dataset/maps/europe5km/dem.map",
        "@ext": 1,
        "@fmap": 1,
        "@namePrefix": "t2",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "/dataset/maps/europe5km/lat.map",
        "@lonMap": "/dataset/maps/europe5km/long.map",
        "@mode": "grib_nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "k2c",
        "@correctionFormula": "p+gem-dem*0.0065",
        "@demMap": "/dataset/maps/europe5km/dem.map",
        "@gem": "(z/9.81)*0.0065",
        "@shortName": "2t"
        }
    }
}
There are four sections of configuration.
#### Aggregation
Defines the aggregation method and step. Method can be accumulation, average or instantaneous.
#### OutMaps
Here you define interpolation method and paths to coordinates PCRaster maps, output unit time, the clone map etc.
#### Interpolation
This is a subelement of OutMaps. Here you define interpolation method (see later for details), paths to coordinates maps.
#### Parameter
In this section, you configure the parameter to select by using its shortName, as stored in GRIB file. You also configure conversion with applyConversion property set to a conversion id. Parameter shortName must be already configured in ~/.pyg2p/parameters.json along with conversion ids.
If you need to apply correction based on DEM files and geopotentials, you can configure formulas and the path to DEM map.
#### Path configuration
You can use variables in JSON files to define paths. Variables can be configured in .conf files under ~/.pyg2p/ folder.
/home/domenico/.pyg2p/myconf.conf
EUROPE_MAPS=/dataset/maps/europe5km
DEM_MAP=/dataset/maps/dem05.map
EUROPE_DEM=/dataset/maps/europe/dem.map
EUROPE_LAT=/dataset/maps/europe/lat.map
EUROPE_LON=/dataset/maps/europe/long.map

Usage of user defined paths in JSON command file:

   { "Execution": {
        "@name": "eue_t24",
        "Aggregation": {
        "@step": 24,
        "@type": "average"
        },
        "OutMaps": {
“@format”: “netcdf”,
        "@cloneMap": "{EUROPE_MAPS}/lat.map",
        "@ext": 1,
        "@fmap": 1,
        "@namePrefix": "pT24",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "{EUROPE_MAPS}/lat.map",
        "@lonMap": "{EUROPE_MAPS}/long.map",
        "@mode": "grib_nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "k2c",
        "@correctionFormula": "p+gem-dem*0.0065",
        "@demMap": "{DEM_MAP}",
        "@gem": "(z/9.81)*0.0065",
        "@shortName": "2t"
        }
    }
}

### Full list of options
#### Main structure

Attribute/Tag	Details
name	The short name of the parameter, as it is in the grib file. The application use this to select messages.
Parameter	See relative table
Aggregation	See relative table
OutMaps	See relative table

#### Parameter property

Attribute/Tag	Details
shortName	The parameter short name, as it is in the grib file. Must be configured in the parameters.json file, otherwise the application exits with an error. Main grib selector.
tstart	Optional grib selectors perturbationNumber, tstart, tend, dataDate and dataTime can also be issued via command line arguments (-m, -s, -e, -D, -T), which overwrite the ones in the execution JSON file.
tend
perturbationNumber
dataDate
dataTime
level
applyConversion	The conversion id to apply, as in the parameters.json file for the parameter to select. The combination parameter/conversion must be properly configured in parmaters.json file, otherwise the application exits with an error.
correctionFormula[1]	Formula to use for parameter correction with p, gem, dem variables, representing parameter value, converted geopotential to gem, and DEM map value. E.g.: p+gem*0.0065-dem*0.0065
demMap	The dem map used for correction.
gem	Formula for geopotential conversion for correction.
[1] When configuring correction, all properties gem, correctionFormula, and demMap must be present.

#### OutMaps property

Attribute/Tag	Details
cloneMap	The clone map with area (must have a REAL cell type and missing values for points outside area of interest. A dem map works fine. A typical area boolean map will not).
unitTime	Time unit in hours of output maps. Tipical value is 24 (daily maps).
format	Output file format. Default 'pcraster'. Available formats are 'pcraster', 'netcdf'.
namePrefix	Prefix for maps. Default is parameter shortName.
fmap	First map number. Default 1.
Interpolation	See relative table.
ext	Extension mode. It's the integer number defining the step numbers to skip when writing maps. Same as old grib2pcraster. Default 1.

#### Aggregation property

Attribute/Tag	Details
step	Step of aggregation in hours.
type	Type of aggregation (it was Manipulation in grib2pcraster). It can be average or accumulation.
forceZeroArray	Optional. In case of “accumulation”, and only then, if this attribute is set to”y” (or any value different from “false”, “False”, “FALSE”, “no”, “NO”, “No”, “0”), the program will use a zero array as message at step 0 to compute the first map, even if the GRIB file has a step 0 message.

#### Interpolation property

Attribute/Tag	Details
mode	Interpolation mode. Possible values are: “nearest”, “invdist”, “grib_nearest”, “grib_invdist”
latMap	PCRaster map of target latitudes.
lonMap	PCRaster map of target longitudes.
intertableDir	Alternative home folder for interpolation lookup tables, where pyg2p will load/save intertables. Folder must be existing. If not set, pyg2p will use intertables from ~/.pyg2p/intertables/

## Usage
To use the application, after the main configuration you need to configure a template JSON file for each type of extraction you need to perform.
### Grabbing information from GRIB files.
To configure the application and compile your JSON templates, you might need to know the variable shortName as stored in the input GRIB file you're using or in the geopotential GRIB. Just execute the following GRIB tool command:
grib_get -p shortName /path/to/grib

Other keys you would to know for configuration or debugging purposes are:
- startStep
- endStep (for instantaneous messages, it can be the same of startStep)
- perturbationNumber (the EPS member number)
- stepType (type of field: instantaneous: 'instant', average: 'avg', cumulated: 'cumul')
- longitudeOfFirstGridPointInDegrees
- longitudeOfLastGridPointInDegrees
- latitudeOfFirstGridPointInDegrees
- latiitudeOfLastGridPointInDegrees
- Ni (it can be missing)
- Nj (it states the resolution: it's the number of points along the meridian)
- numberOfValues
- gridType (e.g.: regular_ll, reduced_gg, rotated_ll)
See Mapping variables section in Appendix B – mapping between grib2pcraster and pyg2p for further information.
### Input arguments
If you run pyg2p without arguments, it shows help of all input arguments.
usage: pyg2p [-h] [-c json_file] [-o out_dir] [-i input_file]
        [-I input_file_2nd] [-s tstart] [-e tend] [-m eps_member]
        [-T data_time] [-D data_date] [-f fmap] [-F format] [-x extension_step]
        [-n outfiles_prefix] [-l log_level] [-N intertable_dir] [-B] [-X]
        [-t cmds_file] [-g geopotential] [-C path] [-z path] [-W dataset]

Execute the grib to pcraster conversion using parameters from the input json
configuration. Read user manual.

optional arguments:
  -h, --help show this help message and exit
  -c json_file, --commandsFile json_file
        Path to json command file
  -o out_dir, --outDir out_dir
        Path where output maps will be created.
  -i input_file, --inputFile input_file
        Path to input grib.
  -I input_file_2nd, --inputFile2 input_file_2nd
        Path to 2nd resolution input grib.
  -s tstart, --start tstart
        Grib timestep start. It overwrites the tstart in json
        execution file.
  -e tend, --end tend Grib timestep end. It overwrites the tend in json
        execution file.
  -m eps_member, --perturbationNumber eps_member
        eps member number
  -T data_time, --dataTime data_time
        To select messages by dataTime key value
  -D data_date, --dataDate data_date
        <YYYYMMDD> to select messages by dataDate key value
  -f fmap, --fmap fmap First map number
 -F format, --format format
        Output format. Available options: netcdf, pcraster.
        Default pcraster
  -x extension_step, --ext extension_step
        Extension number step
  -n outfiles_prefix, --namePrefix outfiles_prefix
        Prefix name for maps
  -l log_level, --loggerLevel log_level
        Console logging level
  -N intertable_dir, --intertableDir intertable_dir
        interpolation tables dir
  -B, --createIntertable
        create intertable file
  -X, --interpolationParallel
        Use parallelization tools to make interpolation
        faster.If -B option is not passed or intertable
        already exists it does not have any effect.
  -t cmds_file, --test cmds_file
        Path to a text file containing list of commands,
        defining a battery of tests. Then it will create diff
        pcraster maps and log alerts if differences are higher
        than a threshold (edit configuration in test.json)
  -g geopotential, --addGeopotential geopotential
        Add the file to geopotentials.json configuration file,
        to use for correction. The file will be copied into
        the right folder (configuration/geopotentials) Note:
        shortName of geopotential must be "fis" or "z"
  -C path, --convertConf path
        Convert old xml configuration to new json format
  -z path, --convertIntertables path
        Convert old pyg2p intertables to new version and copy
        to user folders
  -W dataset, --downloadConf dataset
        Download intertables and geopotentials (FTP settings
        defined in ftp.json)

Usage examples:
pyg2p -c ./exec1.json -i ./input.grib -o /out/dir -s 12 -e 36 -F netcdf
pyg2p -c ./exec2.json -i ./input.grib -o /out/dir -m 10 -l INFO --format netcdf
pyg2p -c ./exec3.json -i ./input.grib -I /input2ndres.grib -o /out/dir -m 10 -l DEBUG
pyg2p -g /path/to/geopotential/grib/file # add geopotential to configuration
pyg2p -t /path/to/test/commands.txt
pyg2p -h

Note: Even if 'netcdf' format is used for output, paths to PCRaster clone/area, latitudes and longitudes maps have to be setup in any case.
### Check output maps
After the execution, you can check output maps by using the PCRaster[2] Aguila viewer for PCRaster maps or the NASA Panoply[3] viewer for NetCDF files.
[2] http://pcraster.geo.uu.nl/
[3] http://www.giss.nasa.gov/tools/panoply/

aguila /dataset/testdiffmaps/eueT24/pT240000.001

./panoply.sh /dataset/octahedral/out/grib_vs_scipy/global/ta/p_2016-09-25_average.nc

Maps will be written in the folder specified by -o input argument. If this is missing, you will find maps in the folder where you launched the application (./).

Refer to official documentation for further information about Aguila and Panoply.
## Interpolation modes
Interpolation is configured in JSON execution templates using the Interpolation attribute inside OutMaps.
There are four interpolation methods available. Two are using GRIB_API nearest neighbours routines while the other two leverage on Scipy kd_tree module.
Note: GRIB_API does not implement nearest neighbours routing for rotated grids. You have to use scipy methods and regular target grids (i.e.: latitudes and longitudes PCRaster maps).
### Intertable creation
Interpolation will use precompiled intertables. They will be found in the path configured in INTERTABLES folder (take into account that can potentially contains gigabytes of files) or in global data path. You can also define an alternate intertables directory with -N argument (or @intertableDir attribute in JSON template).
If interlookup table doesn't exist, the application will create one into INTERTABLES folder and update intertables.json configuration only if -B option is passed, otherwise program will exit.
Be aware that for certain combination of grid and maps, the creation of the interlookup table (which is a numpy array saved in a binary file) could take several hours or even days for GRIB interpolation methods. To have better performances (up to x6 of gain) you can pass -X option to enable parallel processing.
Performances are not comparable with scipy based interpolation (seconds or minutes) but this option could not be viable for all GRIB inputs.
### GRIB API interpolation methods
To configure the interpolation method for conversion, set the @mode attribute in Execution/OutMaps/Interpolation property.

grib_nearest:
This method uses GRIB API to perform nearest neighbour query.
To configure this method, define:
"Interpolation": {
    "@latMap": "/dataset/maps/europe5km/lat.map",
    "@lonMap": "/dataset/maps/europe5km/long.map",
    "@mode": "grib_nearest"
}

grib_invdist:
It uses GRIB_API to query for four neighbours and relative distances. It applies inverse distance calculation to compute the final value.
To configure this method:
"Interpolation": {
    "@latMap": "/dataset/maps/europe5km/lat.map",
    "@lonMap": "/dataset/maps/europe5km/long.map",
    "@mode": "grib_invdist"
}
### Scipy interpolation methods

nearest:
It's the same nearest neighbour algorithm of grib_nearest but it uses the scipy kd_tree[4] module to obtain neighbours and distances.
[4] http://docs.scipy.org/doc/scipy/reference/generated/scipy.spatial.KDTree.html
"Interpolation": {
    "@latMap": "/dataset/maps/europe5km/lat.map",
    "@lonMap": "/dataset/maps/europe5km/long.map",
    "@mode": "nearest"
}

invdist:
It's the inverse distance algorithm with scipy.kd_tree , using 8 neighbours.
"Interpolation": {
    "@latMap": "/dataset/maps/europe5km/lat.map",
    "@lonMap": "/dataset/maps/europe5km/long.map",
    "@mode": "invdist"
}

Attributes p, leafsize and eps for the kd tree algorithm are default in scipy library:
Attribute	Details
p	2 (Euclidean metric)
eps	0
leafsize	10

### OutMaps configuration
Interpolation is configured under the outMaps tag. With additional attributes, you also configure resulting PCRaster maps. Output dir is ./ by default or you can set it via command line using the option -o (--outDir).

Attribute	Details
namePrefix	Prefix name for output map files. Default is the value of shortName key.
unitTime	Unit time in hours for results. This is used during aggregation operations.
fmap	Extension number for the first map. Default 1.
ext	Extension mode. It's the integer number defining the step numbers to skip when writing maps. Same as old grib2pcraster. Default 1.
cloneMap	Path to a PCRaster clone map, needed by PCRaster libraries to write a new map on disk.

## Aggregation

Values from grib files can be aggregated before to write the final PCRaster maps. There are two kinds of aggregation available: average and accumulation. The JSON configuration in the execution file will look like:

"Aggregation": {
    "@type": "average"
},

To better understand what these two types of aggregations do, the DEBUG output of execution is presented later in same paragraph.
### Average

Temperatures are often extracted as averages on 24 hours or 6 hours. Here's a typical execution configuration and the output of interest:
#### cosmo_t24.json:

{
    "Execution": {
        "@name": "cosmo_T24",
        "Aggregation": {
        "@step": 24,
        "@type": "average"
        },
        "OutMaps": {
        "@cloneMap": "/dataset/maps/europe/dem.map",
        "@ext": 4,
        "@fmap": 1,
        "@namePrefix": "T24",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "/dataset/maps/europe/lat.map",
        "@lonMap": "/dataset/maps/europe/lon.map",
        "@mode": "nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "k2c",
        "@correctionFormula": "p+gem-dem*0.0065",
        "@demMap": "/dataset/maps/europe/dem.map",
        "@gem": "(z/9.81)*0.0065",
        "@shortName": "2t"
        }
    }
}
#### Command:

pyg2p -l DEBUG -c /execution_templates/cosmo_t24.json -i /dataset/cosmo/2012111912_pf10_t2.grb -o ./cosmo -m 10
#### ext parameter

ext value will affect numbering of output maps.
[2013-07-12 00:06:18,545] :./cosmo/T24a0000.001 written!
[2013-07-12 00:06:18,811] :./cosmo/T24a0000.005 written!
[2013-07-12 00:06:19,079] :./cosmo/T24a0000.009 written!
[2013-07-12 00:06:19,349] :./cosmo/T24a0000.013 written!
[2013-07-12 00:06:19,620] :./cosmo/T24a0000.017 written!

This is needed because we performed 24 hours average over 6 hourly steps.
### Accumulation

For precipitation values, accumulation over 6 or 24 hours is often performed. Here's an example of configuration and execution output in DEBUG mode.
#### Configuration dwd_r06.json:

{
    {"Execution": {
        "@name": "dwd_rain_gsp",
        "Aggregation": {
        "@step": 6,
        "@type": "accumulation"
        },
        "OutMaps": {
        "@cloneMap": "/dataset/maps/europe/dem.map",
        "@fmap": 1,
        "@namePrefix": "pR06",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "/dataset/maps/europe/lat.map",
        "@lonMap": "/dataset/maps/europe/lon.map",
        "@mode": "nearest"
        }
        },
        "Parameter": {
        "@shortName": "RAIN_GSP",
        "@tend": 18,
        "@tstart": 12
        }
    }
}
#### Command:

pyg2p -l DEBUG -c /execution_templates/dwd_r06.json -i /dataset/dwd/2012111912_pf10_tp.grb -o ./cosmo -m 10
#### Output:

[2013-07-11 23:33:19,646] : Opening the GRIBReader for /dataset/dwd/grib/dwd_grib1_ispra_LME_2012111900
[2013-07-11 23:33:19,859] : Grib input step 1 [type of step: accum]
[2013-07-11 23:33:19,859] : Gribs from 0 to 78
...
...
[2013-07-11 23:33:20,299] : ******** **** MANIPULATION **** *************
[2013-07-11 23:33:20,299] : Accumulation at resolution: 657
[2013-07-11 23:33:20,300] : out[s:6 e:12 res:657 step-lenght:6] = grib:12 - grib:6 * (24/6))
[2013-07-11 23:33:20,316] : out[s:12 e:18 res:657 step-lenght:6] = grib:18 - grib:12 * (24/6))

Note: If you want to perform accumulation from Ts to Te with an aggregation step Ta, and Ts-Ta=0 (e.g. Ts=6h, Te=48h, Ta=6h), the program will select the first message at step 0 if present in the GRIB file, while you would use a zero values message instead.
To use a zero values array, set the attribute forceZeroArray to ”true” in the Aggregation configuration element.
For some DWD[5] and COSMO[6] accumulated precipitation files, the first zero message is an instant precipitation and the decision at EFAS was to use a zero message, as it happens for UKMO[7] extractions, where input GRIB files don't have a first zero step message.
[5] http://www.dwd.de/
[6] http://www.cosmo-model.org/
[7] http://www.metoffice.gov.uk/

$ grib_get -p units,name,stepRange,shortName,stepType 2012111912_pf10_tp.grb
kg m**-2 Total Precipitation 0 tp instant
kg m**-2 Total Precipitation 0-6 tp accum
kg m**-2 Total Precipitation 0-12 tp accum
kg m**-2 Total Precipitation 0-18 tp accum
…
kg m**-2 Total Precipitation 0-48 tp accum

## Correction

Values from grib files can be corrected with respect to their altitude coordinate (Lapse rate formulas). Formulas will use also a geopotential value (to read from a GRIB file, see later in this chapter for configuration).
Correction has to be configured in the Parameter element, with three mandatory attributes.
- correctionFormula (the formula used for correction, with input variables parameter value (p), gem, and dem value.
- gem (the formula to obtain gem value from geopotential z value)
- demMap (path to the DEM PCRaster map)
Note: formulas must be written in python notation.
Tested configurations are only for temperature and are specified as follows:

Temperature correction:

"Parameter": {
        "@applyConversion": "k2c",
    "@correctionFormula": "p+gem-dem*0.0065",
    "@demMap": "/dataset/maps/europe/dem.map",
    "@gem": "(z/9.81)*0.0065",
    "@shortName": "2t"
}
A more complicated correction formula:

"Parameter": {
        "@applyConversion": "k2c",
    "@correctionFormula": "p/gem*(10**((-0.159)*dem/1000))",
    "@demMap": "/dataset/maps/europe/dem.map",
    "@gem": "(10**((-0.159)*(z/9.81)/1000))",
    "@shortName": "2t"
}
### How to write formulas

z is the geopotential value as read from the grib file
gem is the value resulting from the formula specified in gem attribute
I.e.: (gem="(10**((-0.159)*(z/9.81)/1000)))”
dem is the dem value as read from the PCRaster map

Be aware that if your dem map has directions values, those will be replicated in the final map.
### Which geopotential file is used?
The application will try to find a geopotential message in input GRIB file. If a geopotential message is not found, pyg2p will select a geopotential file from user or global data paths, by selecting filename from configuration according the geodetic attributes of GRIB message. If it doesn't find any suitable grib file, application will exit with an error message.
Geodetic attributes compose the key id in the JSON configuration (note the $ delimiter):

longitudeOfFirstGridPointInDegrees$longitudeOfLastGridPointInDegrees$Ni$Nj$numberOfValues$gridType

If you want to add another geopotential file to the configuration, just execute the command:

pyg2p -g /path/to/geopotential/grib/file

The application will copy the geopotential GRIB file into GEOPOTENTIALS folder (under user home directory) and will also add the proper JSON configuration to geopotentials.json file.
## Conversion

Values from GRIB files can be converted before to write final output maps. Conversions are configured in the parameters.json file for each parameter (ie. shortName). The right conversion formula will be selected using the id specified in the applyConversion attribute, and the shortName attribute of the parameter that is going to be extracted and converted.
Refer to Parameter configuration paragraph for details.
## Logging

Console logger level is INFO by default and can be optionally set by using -l (or –loggerLevel) input argument.
Possible logger level values are ERROR, WARN, INFO, DEBUG, in increasing order of verbosity .
## pyg2p API

From version 1.3, pyg2p comes with a simple API to import and use from other python programs (e.g. pyEfas).
The pyg2p API is intended to mimic the pyg2p.py script execution from command line so it provides a Command class with methods to set input parameters and a run_command(cmd) module level function to execute pyg2p.
### Setting execution parameters
First, create a pyg2p command:

>>> from pyg2p.main import api
>>> command = api.command()

Then, set up the execution parameters using a chain of methods or single calls:

>>>command.with_cmdpath('a.json')
>>>command.with_inputfile('0.grb')
>>>command.with_log_level('ERROR').with_out_format('netcdf')
>>>command.with_outdir('/dataout/').with_tstart('6').with_tend('24').with_eps('10').with_fmap('1')
>>>command.with_ext('4')
>>> print(str(command))
pyg2p.py -c a.json -e 240 -f 1 -i 0.grb -l ERROR -m 10 -o /dataout/test -s 6 -x 4 -F netcdf

You can also create a command object using the input arguments as you would do when execute pyg2p from shell:

>>>args_string = '-l ERROR -c /pyg2p_git/execution_templates_devel/eue_t24.json -i /dataset/test_2013330702/EpsN320-2013063000.grb -o /dataset/testdiffmaps/eueT24 -m 10'
 >>>command2 = api.command(args_string)

### Execute

Use the run_command function from pyg2p module. This will delegate the main method, without shell execution.

>>>ret = api.run_command(command)

The function returns the same value pyg2p returns if executed from shell (0 for correct executions, included those for which messages are not found).
### Adding geopotential file to configuration

You can add a geopotential file to configuration from pyg2p API as well, using Configuration classes:

>>> from pyg2p.main.config import UserConfiguration, GeopotentialsConfiguration
>>> user=UserConfiguration()
>>> geopotentials=GeopotentialsConfiguration(user)
>>> geopotentials.add('path/to/geopotential.grib')

The result will be the same of pyg2p -g path/to/geopotential.grib.

## Appendix A - Execution JSON files Examples

This paragraph will explain typical execution json configurations.
#### Example 1: Correction with dem and geopotentials

pyg2p -c example1.json -i /dataset/cosmo/2012111912_pf2_t2.grb -o ./out_1
example1.json

{
        "Execution": {
        "@name": "eue_t24",
        "Aggregation": {
        "@step": 24,
        "@type": "average"
        },
        "OutMaps": {
        "@cloneMap": "{EUROPE_MAPS}/lat.map",
        "@ext": 1,
        "@fmap": 1,
        "@namePrefix": "pT24",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "{EUROPE_MAPS}/lat.map",
        "@lonMap": "{EUROPE_MAPS}/long.map",
        "@mode": "grib_nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "k2c",
        "@correctionFormula": "p+gem-dem*0.0065",
        "@demMap": "{DEM_MAP}",
        "@gem": "(z/9.81)*0.0065",
        "@shortName": "2t"
        }
    }
}

This configuration, will select the 2t parameter from time step 0 to 12, out of a cosmo t2 file. Values will be corrected using the dem map and a geopotential file as in geopotentials.json configuration.
Maps will be written under ./out_1 folder (the folder will be created if not existing yet). The clone map is set as same as dem.map. Note that paths to maps uses variables EUROPE_MAPS and DEM_MAP. You will set these variables in myconf.conf file under ~/.pyg2p/ folder.
The original values will be converted using the conversion “k2c”. This conversion must be configured in the parameters.json file for the variable which is being extracted (2t). See Parameter property configuration at Parameter.

The interpolation method is grib_nearest. Latitudes and longitudes values will be used only if the interpolation lookup table (intertable) hasn't be created yet but it's mandatory to set latMap and lonMap because the application uses their metadata raster attributes to select the right intertable.
The table filename to be read and used for interpolation is automatically found by the application, so there is no need to specify it in configuration. However, lat and lon maps are mandatory configuration attributes.

#### Example 2: Dealing with multiresolution files
pyg2p -c example1.json -i 20130325_en0to10.grib -I 20130325_en11to15.grib -o ./out_2
Performs accumulation 24 hours out of sro values of two input grib files having different vertical resolutions. You can also feed pyg2p with a single multiresolution file.
pyg2p -c example1.json -i 20130325_sro_0to15.grib o ./out_2 -m 0

    {"Execution": {
        "@name": "multi_sro",
        "Aggregation": {
        "@step": 24,
        "@type": "accumulation"
        },
        "OutMaps": {
        "@cloneMap": "/dataset/maps/global/dem.map",
        "@fmap": 1,
        "@namePrefix": "psro",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "/dataset/maps/global/lat.map",
        "@lonMap": "/dataset/maps/global/lon.map",
        "@mode": "grib_nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "m2mm",
        "@shortName": "sro",
        "@tend": 360,
        "@tstart": 0
        }
    }
}

This execution configuration will extract global overlapping messages sro (perturbation number 0) from two files at different resolution.
Values will be converted using “tomm” conversion and maps (interpolation used here is grib_nearest) will be written under ./out_6 folder.

#### Example 3: Accumulation 24 hours
./pyg2p.py -i /dataset/eue/EpsN320-2012112000.grb -o ./out_eue -c execution_file_examples/execution_9.json

  { "Execution": {
        "@name": "eue_tp",
        "Aggregation": {
        "@step": 24,
        "@type": "accumulation"
        },
        "OutMaps": {
        "@cloneMap": "/dataset/maps/europe5km/lat.map",
        "@fmap": 1,
        "@namePrefix": "pR24",
        "@unitTime": 24,
        "Interpolation": {
        "@latMap": "/dataset/maps/europe5km/lat.map",
        "@lonMap": "/dataset/maps/europe5km/long.map",
        "@mode": "grib_nearest"
        }
        },
        "Parameter": {
        "@applyConversion": "tomm",
        "@shortName": "tp"
        }
    }
}

## Appendix B – mapping between grib2pcraster and pyg2p

This appendix aims to help to migrate from grib2pcraster to pyg2p.
### Differences in glossary
- The Manipulation as intended in grib2pcraster becomes Aggregation in pyg2c; if you read the term manipulation in the pyg2c documentation, that means a more generic term, including correction and conversion. Anyway, if you read the python code, the python class which performs aggregation is called Manipulator itself.
- What it's called TypeOfField in grib2pcraster becomes stepType in pyg2p (as for the GRIB standard). It defines the aggregated nature of the variable which can be instant, averaged, or cumulated.
- In grib2pcraster, the variable to extract is called parameter and it's referenced by a couple of numbers: x.y, where:
  - x is the value of the indicatorOfParameter key as found in the GRIB message
  - y is an internal number identifying the TableVersion as found in the parameters.xml file of grib2pcraster.
- In pyg2p, while the Parameter term was retained, it is identified by the shortName key as found in the GRIB message. This is an independent version key and it's only related to the variable itself and not to the generating centre of the file, since this is already coded in GRIB API tables. That is, in pyg2p the concepts of generating centre and table parameter versions don't need to exist.
### Mapping variables
To “translate” the parameter code x.y used in grib2pcraster to the shortName form of pyg2c, just follow these simple steps:
1. Identify the parameter in grib2pcraster's parameters.xml file using y to find the gribTablesVersionNo and x to find the single item Param.
2. Take note of abbreviation and field description strings of the Param above.
3. Use some basic GRIB tools (and meteorological) skills to find the shortName value of the grib:
  grib_get -p shortName,parameterName /path/to/grib/file.grib2
### Known parameters mapping with conversions
Variable	grib2pcraster selectors (indicatorOfParameter.gribTablesVersionNo)	pyg2p.py shortName	Configured conversions in grib2pcraster
2 meters Dew-point	17.2 / 168.128	2D	x-273.15
2 meters Temperature	11.2 / 500011.0 / 167.128	t_2m / td_2m / 2t	x-273.15
Total precipitation	61.2 / 228.128	tp	Only cut off / x*1000 + cut off
Latent heat flux	500086.0 / 121.2	alhfl_s	x*(-0.0353) + cut off [default] / x*(-0.00147) + cut off
Surface Latent heat flux	147.128	slhf	No conversion
Surface Runoff	8.230 / 8.128	sro	x*1000 + cut off
Sub-Surface Runoff	9.230 / 9.128	ssro	x*1000 + cut off
Large scale precipitation	142.128	lsp	x*1000 + cut off
Convective precipitation	143.128	Not tested. It needs to be added to parameters.xml if used.	x*1000 + cut off
Evaporation	182.128	e	x*(-1000)
Runoff	205.128	Not tested. It needs to be added to parameters.xml if used.	x*1000 + cut off (not as default, it needs to be set by command line with --unit parameter)
Surface precipitation amount, rain, grid scale	102.201	rain_gsp	Only cut off
Surface precipitation amount, rain, convective	113.201	rain_con	Only cut off
Large scale rain rate	500134.0	Not tested. It needs to be added to parameters.xml if used.	Only cut off
Snow fall	144.128	Not tested. It needs to be added to parameters.xml if used.	x*1000
Snow depth	141.128	Not tested. It needs to be added to parameters.xml if used.	X*1000 (not as default, it needs to be set by command line with --unit parameter)

### Execution parameters mapping
Argument	grib2pcraster	pyg2p.py
Input file	-i	-i
Variable	-p x.y	json[8] (shortName)
Output directory	-o	-o
EPS perturbationNumber	-m	-m
Variable level	--level	json
Aggregation type	Default in parameters.xml. Overwriting with --ma	json (type)
Aggregation step	-t	json (step)
Start step	-s	-s or json (tstart)
End step	-e	-e or json (tend)
Output map unittime	--unittime	json (unitTime)
Interpolation	-r,-l,-a or –intertable	json (see relative section in this manual).
Conversion	parameters.xml	parameters.json and json command file (applyConversion)
Correction	Two formulas hardcoded and configured by default in parameters.xml or with --temp and --evap.	json (attributes correctionFormula, gem, dem)
Map extension naming	--fmap, --ext	json
Map prefix name	-n	json
Logging	--report. Loggers directory is under program installation folder	Console logger level overwritable with -l (default is INFO).
[8] In this table, “json” means that the corresponding parameter configuration is in the execution json template where you configure your extraction and pass to the pyg2p with the -c input argument. If not indicated otherwise, the json tag/attribute name is the same as the grib2pcraster input argument (e.g.: --level=10 becomes the json attribute level=”10”).

### Difference in dealing with multiresolution
Multiresolution extraction can be made in one step with pyg2p, using both -i and -I for input files or even a single multiresolution file. The grib2pcraster application needs to perform two executions, instead.
### Differences in Correction
There is a sort of bug in grib2pcraster when come to correction, since the dem values it uses are stored in its interlookup tables and, if the DEM has changed for some reasons, the corrected values will be wrong unless the interlookup table is not regenerated using the new DEM map.
However, here the main difference is that the correction formulas are editable directly by the user in pyg2p.
### Differences in Aggregation
The type of aggregation and its step window must be specified in pyg2p, using the Aggregation attribute.
In grib2pcraster, instead, the type of aggregation for the specific variable is being extract (i.e. manipulation) is read from ManipulationFlag attribute in parameters.xml file: “1” for average and “2” for accumulation. The step window is 24 hours by default and it can be overwritten with -t parameter.

### Differences in Interpolation
Resampling of grids in grib2pcraster is made using GRIB API. Available interpolation methods are:
- nearest neighbours
- inverse distance
The interpolation table file is declared with the input argument –intertable, or otherwise by configuration, using one of the tables in interpolation.xml.
In pyg2p there are two additional resampling modes (see the relative Interpolation modes paragraph in this document). Results are very similar to GRIB_API based interpolation methods but interlookup table is being created in seconds rather than hours (in our tests, interlookup table creation for high resolution or global scale grids take almost two days with GRIB_API methods while it takes one minute with scipy based methods).
They are nearest and invdist modes, performed using scipy routines to find neighbours and distances.
Interlookup tables are read/written by default using ~/.pyg2p/intertables as folder where to load existing intertables or save new ones. An alternative folder can be specified using the intertableDir attribute in the Interpolation property of the json template configuration.

## Appendix C – Glossary

Brief description of terms you find in this manual, with their synonims.

Term	Synonims	Description
Interpolation lookup table	Intertable, interlookup table	It's a numpy binary file containing indexes correspondences and coefficients/distances. Each combination of GRIB grid/PCRaster target coordinates maps/Interpolation mode has its own intertable. Since there are four interpolation modes using intertables, there can be four different intertables for each combination of GRIB grid/PCRaster lat/lon maps.
Aggregation		Average or accumulation
Interpolation	Resampling	Resampling between the original GRIB grid and the target raster lat/lon coordinates.
Execution JSON template file	Execution template, commands file, execution file, json template, json configuration	The JSON file where most of execution parameters are configured. It's being passed by the mandatory CLI argument -c.
Parameter	Variable	The meteorological variable stored in the input grib file.
Command line Input argument	Input argument, CLI argument, option	Input arguments to the application passed via command line. They are -i,-I,-o,-m,-l,-d,-c
Execution parameter	Parameter, input argument	All configured options (via CLI or json files) that define the execution context.
GRIB grid	Grid	It's the set of geodetic attributes identifying the coordinate system and the specific projected area. The set includes gridType, first and last values of latitude and longitudes, number of points along the meridian.
GRIB message's gridType	Grid type, grid	It's the specific grid type of the GRIB message and can be regular_rr, regular_ll, rotated_rr, rotated_ll, reduced_ll and so on.
GRIB message	Grib	It's a single message extracted from a GRIB file.
GRIB API		C library (and its wrappers) from ECMWF to deal with grib files.
GRIB file	Grib	An input file encoded using GRIB format.
Geopotential GRIB values	Geopotential	Geopotential values encoded in grib files, used for correction.
Gem value	Gem	In correction, the gem value is being obtained using the formula configured with gem property, where z is the geopotential value. E.g. gem = “(z/9.81)*0.0065”

## Appendix D – Developer notes
### Developer notes about correction formulas
Previous correction formulas were derived directly from grib2pcraster C code. The need to set up two formulas – one for the gem value and one for the final corrected value (which uses the previously formulated gem value) – exists because the correction formulas are based on DEM and geopotential values. DEM values are in PCRaster format while geopotential data is a GRIB message, which needs to be interpolated before to put it into the correction formula. That means that the correction process is applied in two steps with a split formula as configured.
#### Grib2pcraster correction process:
In this paragraph, some C code is shown from the original grib2pcraster C application.
Geopotential value is read from a grib file as (note the correction):

//correction formula is applied here (it's the gem in pyg2p)
if (intCorrectionFlag == 1)//temperature correction
{
for (i = 0; i < values_len; i++) {
pgeopotential[i] = (pgeopotential[i] / 9.81) * 0.0065;
}
} else if (intCorrectionFlag == 2)//evap correction
{
for (i = 0; i < values_len; i++) {
pgeopotential[i] = pgeopotential[i] / 9.81;
pgeopotential[i] = pow(10, ((-0.159) * (pgeopotential[i]) / 1000));
}
}
Then, the actual correction is made during the interpolation process (some not relevant code was removed and comments added to the real code):

//interpolation
float tmpValue = (pGRIBValues[grid[i].indexInGRIBArrNode1]) * (grid[i].CoefficientNode1) + (pGRIBValues[grid[i].indexInGRIBArrNode2]) * (grid[i].CoefficientNode2) + (pGRIBValues[grid[i].indexInGRIBArrNode3]) * (grid[i].CoefficientNode3)
+ (pGRIBValues[grid[i].indexInGRIBArrNode4]) * (grid[i].CoefficientNode4);

if (intCorrectionFlag != 0) {
   //interpolation of geopotential as read before
   float tmpGeo = (geopotential[grid[i].indexInGRIBArrNode1]) * (grid[i].CoefficientNode1) + (geopotential[grid[i].indexInGRIBArrNode2]) * (grid[i].CoefficientNode2) + (geopotential[grid[i].indexInGRIBArrNode3]) * (grid[i].CoefficientNode3)
+ (geopotential[grid[i].indexInGRIBArrNode4]) * (grid[i].CoefficientNode4);

    //correction formula is applied here (the correctionFormula in pyg2p)
   if (intCorrectionFlag == 1)//temperature correction
tmpValue = (tmpValue + tmpGeo) - (grid[i].demValue * 0.0065);
    if (intCorrectionFlag == 2)//evap correction
   tmpValue = (tmpValue / tmpGeo) * (pow(10, ((-0.159) * (grid[i].demValue) / 1000)));
}
//store value in the output array
pPCRasterValues[grid[i].indexInPCRasterArr] = tmpValue;

#### pyg2p correction process

The process in pyg2p is almost the same, that means:

- read geopotential from grib, and apply the correction formula as configured in json execution file (gem=”(z/9.81)*0.0065”)
- interpolate the gem values so obtained to the PCRaster output grid
- read grib values and interpolate them
- apply the final correction formula as configured (correctionFormula=”p+gem-dem*0.0065”)

The only difference is that in pyg2p formulas are configurable, as explained in this chapter (read Configuration manual as well), while in grib2pcraster you can choose, with a binary flag in parameters.json file, between two hard coded formulas (one for temperature and one for evaporation).