# pyg2p Installation Manual

Version	1.2
Author	Domenico Nappo (domenico.nappo(at)gmail.com)
Final Release (Rev. 03)	2013-10-14

## Prerequisites

In order to run pyg2p application, the following python version and packages must be installed.

Most packages need additional requirements such as C libraries properly installed on the computer for the user running the application.

Software Requirement	Purpose	Dependencies
Python 2.7	Execution environment
NumPy 1.7	fast array manipulation	ATLAS + LAPACK libs Python header files / gcc and gfortran compilers
SciPy 0.11	interpolation	ATLAS + LAPACK libs Python header files gcc and gfortran compilers
gribapi	reading grib files, interpolation	GRIB_API
GDAL python	reading and writing pcraster maps	GDAL lib and its requirements.
untangle 1.1	xml parsing

## Installation

1. Decompress the file pyg2p_v.<version>.tar.gz in the <target directory> using tar xzvf pyg2p_v.<version>.tar.gz.
2. cd <target directory> and issue the command python test_reqs.py. If some required packages are missing, install them. If core packages are missing, contact the developer.
3. Modify the first line of pyg2p.py to point to the desired python interpreter if you will execute the application as ./pyg2p.py.
   Otherwise execute the program with /path/to/python ./ pyg2p.py
4. Configure the application (see Configuration Manual).
5. The application is shipped with some configurations of example in execution_templates folder. Just adjust paths and parameters for fire tests. Also, use the -t option for comparing results with the grib2pcraster C application. Read User Manual first.
6. Ready to start.